## Slide 1: RouterOS v5 wireless features
Uldis Cernevskis
MikroTik
2011

## Slide 2: Station-bridge feature
This mode provides support for transparent protocol-independent L2 bridging on station device
This mode is MikroTik proprietary and can't be used to connect other brand devices
RouterOS accepts clients with "station-bridge" mode if "bridge-mode" parameter is enabled in the AP settings
RouterOS v5.0rc11 or newer needed on AP and Station

## Slide 3: Wireless station modes application matrix
 | 802.11 | ROS 802.11 | Nstreme | Nv2
Station | V | V | V | V
Station-wds |  | V | V | V
Station-pseudobridge | V | V | V | 
Station-pseudobridge-clone | V | V | V | 
Station-bridge |  | V | V | V

## Slide 4: Wireless-protocol setting
Value | AP | Client
unspecified | establish nstreme or 802.11 network based on old nstreme setting | connect to nstreme or 802.11 network based on old nstreme setting
any | same as unspecified | scan for all matching networks, no matter what protocol, connect using protocol of chosen network
802.11 | establish 802.11 network | connect to 802.11 networks only
nstreme | establish Nstreme network | connect to Nstreme networks only
nv2 | establish Nv2 network | connect to Nv2 networks only
nv2-nstreme-802.11 | establish Nv2 network | scan for Nv2 networks, if suitable network found - connect, otherwise scan for Nstreme networks, if suitable network found - connect, otherwise scan for 802.11 network and if suitable network found - connect
nv2-nstreme | establish Nv2 network | scan for Nv2 networks, if suitable network found - connect, otherwise scan for Nstreme networks and if suitable network found - connect

## Slide 5: Signal reading for each chain
“signal-strength” - combination of all active chains on the control and extension channels
"signal-strenght-ch0" - chain 0 control channel
"signal-strenght-ch1" - chain 1 control channel
"signal-strenght-ch2" - chain 2 control channel
No separate signal readings for extension channel
Tx chains signal readings currently available only for Nv2

## Slide 6: Frequency-offset feature
Frequency-offset feature is designed for easier frequency selection on wireless cards with built-in frequency converter

## Slide 7: Antenna-mode selection for RB751U and RB751G
RB 751U and RB751G has 3 built-in wireless antennas
  Chain0:
    one antenna for TX
    one antenna for RX
  Chain1:
    one antenna for TX/RX
    external antenna connected to MMCX connector
Note that enabling the external antenna disables the Chain1 built-in antenna

## Slide 8: Antenna-mode selection for RB751U and RB751G

## Slide 9: Spectral Scan/History
Uses RouterOS
Uses Atheros Merlin 802.11n chipset wireless cards
Frequency span depending on card:
  5ghz: 4790-6085mhz
  2ghz: 2182-2549mhz
Scan with 10mhz frequency increments for improved data quality
Audio monitor

## Slide 10: Spectral Scan using the Dude

## Slide 11: LED feature
Wireless signal LEDs supported added for RB400 series, RB711, RB SXT and RB Groove:
  1 LED - on, if wireless client is connected to AP (usually >= -89dBm)
  2 LEDs - on, if signal strength >= -82dBm
  3 LEDs - on, if signal strength >= -75dBm
  4 LEDs - on, if signal strength >= -68dBm
  5 LEDs - on, if signal strength >= -61dBm

## Slide 12: Wireless LEDs on RB SXT and RB Groove

## Slide 13: Nv2 Protocol
Proprietary wireless protocol developed by MikroTik
Based on TDMA (Time Division Multiple Access) media access technology
Works on Atheros chipset cards:
  AR5413 and newer chipset cards (R52)
  N chipset cards (R52n,R52Hn)
Supported from RouterOS v5

## Slide 14: Nv2 TCP routing both direction

## Slide 15: AR9380 chipset support